## Slide 1: Networks & Security Lecture-1
www.corvit.com

## Slide 2: Topics
What is a Network?
Types of Network
Network Topologies
Peer-to-Peer vs Client Server Architecture
Physical Media
What is Internet?
What is a Protocol?
OSI Model
OSI vs TCP/IP
Network Protocols Port Numbers
Network Security
Firewall
www.corvit.com

## Slide 3: What is the Network?
billions of connected computing devices:
  hosts = end systems
  running network apps
communication links
  fiber, copper, radio, satellite
  transmission rate: bandwidth
packet switches: forward packets (chunks of data)
  routers and switches
wired
links
wireless
links
router
smartphone
PC
server
wireless
laptop
mobile network
global ISP
regional ISP
home
network
institutional
network
Communication between different computing devices over a shared medium to exchange data is known as a Network.
www.corvit.com
Notes: <number>

## Slide 4: Network Devices
www.corvit.com

## Slide 5: Types of Network
PAN (Example: Bluetooth)
LAN (Example: Networking in home, office)
WAN (Example: Internet )
WLAN (Example: Wi-Fi)
CAN (Example: University Network )
MAN (Example: Networking between banks in a city.)
SAN (Example: ERP and CRM Environments)
POLAN (Example: Can be used in Home, Offices, Universities, Hotels etc)
EPN (Example: IT Companies Network)
VPN (Example: Telecommuters)
www.corvit.com
Notes: https://www.belden.com/blogs/smart-building/network-types

## Slide 6: Network Topologies
Point-to-Point
Bus
Star
Ring
www.corvit.com
Notes: https://www.tutorialspoint.com/data_communication_computer_network/computer_network_topologies.htm

## Slide 7: Network Topologies
Mesh
Tree
Daisy Chain
Hybrid
www.corvit.com

## Slide 8: Peer-to-Peer vs Client Server Architecture
www.corvit.com

## Slide 9: Physical media
bit: propagates between transmitter/receiver pairs
physical link: what lies between transmitter & receiver
guided media:
  signals propagate in solid media: copper, fiber, coax
unguided media:
  signals propagate freely, e.g., radio
twisted pair (TP)
two insulated copper wires
  Category 5: 100 Mbps, 1 Gbps Ethernet
  Category 6: 10Gbps
www.corvit.com

## Slide 10: Physical Media: Coax, Fiber
coaxial cable:
two concentric copper conductors
bidirectional
broadband:
  multiple channels on cable
  HFC
fiber optic cable:
glass fiber carrying light pulses, each pulse a bit
high-speed operation:
  high-speed point-to-point transmission (e.g., 10’s-100’s Gbps transmission rate)
low error rate:
  repeaters spaced far apart
  immune to electromagnetic noise
www.corvit.com

## Slide 11: Physical Media: Radio
signal carried in electromagnetic spectrum
no physical “wire”
bidirectional
propagation environment effects:
  reflection
  obstruction by objects
  interference
radio link types:
terrestrial microwave
  e.g. up to 45 Mbps channels
LAN (e.g., WiFi)
  54 Mbps
wide-area (e.g., cellular)
  4G cellular: ~ 10 Mbps
satellite
  Kbps to 45Mbps channel (or multiple smaller channels)
  270 msec end-end delay
  geosynchronous versus low altitude
www.corvit.com

## Slide 12
Internet: “network of networks”
  Interconnected ISPs
protocols control sending, receiving of messages
  e.g., TCP, IP, HTTP, Skype, 802.11
Internet standards
  RFC: Request for comments
  IETF: Internet Engineering Task Force
What is the Internet?
mobile network
global ISP
regional ISP
home
network
institutional
network
www.corvit.com

## Slide 13: Internet structure: network of networks
End systems connect to Internet via access ISPs (Internet Service Providers)
  residential, company and university ISPs
Access ISPs in turn must be interconnected.
  so that any two hosts can send packets to each other
Resulting network of networks is very complex
  evolution was driven by economics and national policies
Let’s take a stepwise approach to describe current Internet structure
www.corvit.com

## Slide 14: Internet structure: network of networks
Question: given millions of access ISPs, how to connect them together?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
www.corvit.com

## Slide 15: Internet structure: network of networks
Option: connect each access ISP to every other access ISP?
access
net
access
net
…
…
…
…
…
…
…
…
connecting each access ISP to each other directly doesn’t scale: O(N2) connections.
access
net
access
net
access
net
access
net
access
net
access
net
…
access
net
access
net
access
net
access
net
…
access
net
access
net
access
net
access
net
…
www.corvit.com

## Slide 16: Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
Option: connect each access ISP to one global transit ISP?
Customer and provider ISPs have economic agreement.
global ISP
www.corvit.com

## Slide 17: Internet structure: network of networks
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
But if one global ISP is viable business, there will be competitors ….
access
net
www.corvit.com

## Slide 18: Internet structure: network of networks
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
access
net
But if one global ISP is viable business, there will be competitors …. which must be interconnected
IXP
peering link
Internet exchange point
IXP
www.corvit.com

## Slide 19: Internet structure: network of networks
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
access
net
IXP
IXP
access
net
access
net
access
net
regional net
… and regional networks may arise to connect access nets to ISPs
www.corvit.com

## Slide 20: Internet structure: network of networks
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
access
net
IXP
IXP
access
net
access
net
access
net
regional net
Content provider network
… and content provider networks (e.g., Google, Microsoft, Akamai) may run their own network, to bring services, content close to end users
www.corvit.com

## Slide 21: Internet structure: network of networks
IXP
IXP
IXP
Tier 1 ISP
Tier 1 ISP
Google
Regional ISP
Regional ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
at center: small # of well-connected large networks
  “tier-1” commercial ISPs (e.g., Level 3, Sprint, AT&T, NTT), national & international coverage
  content provider network (e.g., Google): private network that connects it data centers to Internet, often bypassing tier-1, regional ISPs
www.corvit.com

## Slide 22: Internet Structure
www.corvit.com

## Slide 23: What’s a protocol?
human protocols:
“what’s the time?”
“I have a question”
introductions
… specific messages sent
… specific actions taken when messages received, or other events
network protocols:
machines rather than humans
all communication activity in Internet governed by protocols
protocols define format, order of messages sent and received among network entities, and actions taken on message transmission, receipt
www.corvit.com

## Slide 24
a human protocol and a computer network protocol:
Q: other human protocols?
Hi
Hi
Got the
time?
2:00
TCP connection
response
Get http://www.awl.com/kurose-ross
<file>
time
TCP connection
request
What’s a protocol?
www.corvit.com

## Slide 25: OSI Model
The Open Systems Interconnection (OSI) model describes seven layers that computer systems use to communicate over a network.
Each Layer represents a different category of networking functions
www.corvit.com

## Slide 26: OSI vs TCP/IP Model
www.corvit.com

## Slide 27: Encapsulation
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame
www.corvit.com

## Slide 28: Network Protocols
application: supporting network applications
  FTP, SMTP, HTTP, Telnet, SNMP.
transport: process-process data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet, 802.111 (WiFi), PPP, HDLC, Token Ring, Frame Relay, ATM.
physical: bits “on the wire”.
  Fiber Optics, Coax, Microwave, Satellite.
www.corvit.com
Notes: https://www.sce.carleton.ca/netmanage/dcommTutorials/scan05/scan05.html

## Slide 29: Network Protocols Port Numbers
www.corvit.com

## Slide 30: Network security
field of network security:
  how bad guys can attack computer networks
  how we can defend networks against attacks
  how to design architectures that are immune to attacks
Internet not originally designed with (much) security in mind
  original vision: “a group of mutually trusting users attached to a transparent network” 
  Internet protocol designers playing “catch-up”
  security considerations in all layers!
www.corvit.com

## Slide 31: Bad guys: put malware into hosts via Internet
malware can get in host from:
  virus : self-replicating infection by receiving/executing object (e.g., e-mail attachment)
  worm: self-replicating infection by passively receiving object that gets itself executed
spyware malware can record keystrokes, web sites visited, upload info to collection site
infected host can be enrolled in botnet, used for spam. DDoS attacks
www.corvit.com

## Slide 32
target
Denial of Service (DoS): attackers make resources (server, bandwidth) unavailable to legitimate traffic by overwhelming resource with bogus traffic
1. select target
2. break into hosts around the network (see botnet)
3. send packets to target from compromised hosts
Bad guys: attack server, network infrastructure
www.corvit.com

## Slide 33: Bad guys can sniff packets
packet “sniffing”:
  broadcast media (shared Ethernet, wireless)
  promiscuous network interface reads/records all packets (e.g., including passwords!) passing by
A
B
C
src:B dest:A payload
www.corvit.com

## Slide 34: Bad guys can use fake addresses
IP spoofing: send packet with false source address
A
B
C
src:B dest:A payload
www.corvit.com

## Slide 35: Firewall
In computing, a firewall is a network security system that monitors and controls incoming and outgoing network traffic based on predetermined security rules.
A firewall typically establishes a barrier between a trusted network and a n untrusted network such as the internet.
The primary goal of a firewall is to block malicious traffic requests and data packets while allowing legitimate traffic through.
www.corvit.com

## Slide 36: Types of Firewall
Packet Filtering: It is a management program that can block network traffic IP protocol, an IP address and a port a number. This type of firewall is the most basic form of protection and is meant for smaller networks. A small amount of data is analyzed and distributed according to the filter’s standards.
Proxy Service: An early type of firewall device, a proxy firewall serves as the gateway from one network to another for a specific application. Proxy servers can provide additional functionality such as content caching and security by preventing direct connections from outside the network.
Stateful Inspection: A stateful inspection firewall allows or blocks traffic based on state, port and protocol. It monitors all activity from the opening of a connection until it is closed. Filtering decisions are made based on both administrator –defined rules as well as the context, which refers to using information from previous connections and packets belonging to the same connection.
www.corvit.com

## Slide 37: Types of Firewall
Unified Threat Management (UTM) Firewall: The functions of a stateful inspection firewall with intrusion prevention and antivirus. It may also include additional services and often cloud management. UTMs focus on simplicity and ease of use.
Next Generation Firewall (NGFW): Firewalls have evolved beyond simple packet filtering and stateful inspection. Most companies are deploying NGFW to block modern threat such as advanced malware and application-layer attacks. A NGFW includes standard firewall capabilities like stateful inspection, integrated intrusion prevention, application awareness and control to see and block risky apps, upgrade paths to include future information feeds and techniques to address evolving security threats.
www.corvit.com

## Slide 38: Web Application Firewall
A WAF or web application firewall helps protect web applications by filtering and monitoring HTTP traffic between a web application and the Internet.
It typically protects web applications from attacks such as cross-site forgery, cross-site-scripting (XSS), file inclusion, and SQL injection, among others.
A WAF is a protocol layer 7 defense (in the OSI model), and is not designed to defend against all types of attacks. This method of attack mitigation is usually part of a suite of tools which together create a holistic defense against a range of attack vectors.
By deploying a WAF in front of a web application, a shield is placed between the web application and the Internet. While a proxy server protects a client machine’s identity by using an intermediary, a WAF is a type of reverse-proxy, protecting the server from exposure by having clients pass through the WAF before reaching the server.
A WAF operates through a set of rules often called policies.
These policies aim to protect against vulnerabilities in the application by filtering out malicious traffic.
The value of a WAF comes in part from the speed and ease with which policy modification can be implemented, allowing for faster response to varying attack vectors; during a DDoS attack, rate limiting can be quickly implemented by modifying WAF policies.
www.corvit.com

## Slide 39: Web Application Firewall
www.corvit.com